## Slide 1: Inputs and Outputs to Aggregate Production Planning
Aggregate
Production
Planning
Company
Policies
Financial
Constraints
Strategic
Objectives
Units or dollars
subcontracted,
backordered, or
lost
Capacity
Constraints
Size of
Workforce
Production
per month
(in units or $)
Inventory
Levels
Demand
Forecasts

## Slide 2: Material Requirements Planning (MRP)
A computerized inventory control & production planning system
Schedules component items when they are needed - no earlier and no later

## Slide 3: When to Use MRP
Dependent and discrete items
Complex products
Job shop production
Assemble-to-order environments

## Slide 4: MRP Inputs & Outputs
Master Production Schedule
Material
Requirements
Planning
Planned Order Releases
Work Orders
Purchase Orders
Rescheduling Notices
Product
Structure
File
Inventory
Master
File

## Slide 5: MRP Inputs
Master production schedule
Product structure file
Inventory master file

## Slide 6: Master Production Schedule
Drives MRP process with a schedule of finished products
Quantities represent production not demand
Quantities may consist of a combination of customer orders & demand forecasts
Quantities represent what needs to be produced, not what can be produced

## Slide 7: Product Structure Tree
Clipboard
Rivet (2)
Iron Rod (3 in.)
Spring (1)
Spring Steel (10 in.)
Level 0
Level 1
Level 2
Level 3
Bottom Clip (1)
Top Clip (1)
Pivot (1)
Sheet Metal (8 in2)
Clip Assembly (10)
Sheet Metal (8 in2)
Board (1)
Pressboard (1)
Finish (2oz.)

## Slide 8: Indented Bill of Material
LEVEL ITEM Unit of Measure Quantity
0 - - - - Clipboard Ea 1
- 1 - - - Clip Assembly Ea 1
- - 2 - - Top Clip Ea 1
- - - 3 - Sheet Metal In2 8
- - 2 - - Bottom Clip Ea 1
- - - 3 - Sheet Metal In2 8
- - 2 - - Pivot Ea 1
- - - 3 - Iron Rod In 3
- - 2 - - Spring Ea 1
- - - 3 - Spring Steel In 10
- 1 - - - Rivet Ea 2
- 1 - - - Board Ea 1
- - 2 - - Press Board Ea 1
- - 2 - - Finish Oz 2

## Slide 9: Specialized BOMS
Phantom bills
  transient subassemblies
  never stocked
  immediately consumed in next stage
K-bills
  group small, loose parts under pseudoitem #
  reduces paperwork

## Slide 10: Specialized BOMS
Modular bills
  product assembled from major subassemblies & customer options
  modular bill kept for each major subassembly
  simplifies forecasting & planning
  X10 Automobile example
    3 x 8 x 3 x 8 x 4 = 2,304 configurations
    3 + 8 + 3 + 8 + 4 = 26 modular bills

## Slide 11: Inventory Master File
Description Inventory Policy
Item Board Lead time 2
Item no. 7341 Annual demand 5,000
Item type Manuf. Holding cost 1
Prod/sales Ass’y Ordering/setup cost 50
Value class B Safety stock 25
Buyer/planner RSR Reorder point 39
Vendor 07142 EOQ 316
Phantom code N Minimum order qty 100
Unit price/cost 1.25 Maximum order qty 500
Pegging Y Multiple order qty 100

## Slide 12: Inventory Master File, Con’t.
Physical Inventory Usage/Sales
On hand 100 YTD usage/sales 1,100
Location W142 MTD usage/sales 75
On order 50 YTD receipts 1,200
Allocated 75 MTD receipts 0
Cycle 3 Last receipt 8/25
Difference -2 Last issue 10/5
Codes
Cost acct. 00754
Routing 00326
Engr 07142

## Slide 13: Inventory Accuracy
1. Maintain orderly stockrooms
2. Control access to stockrooms
3. Establish & enforce procedures for inventory withdrawal
4. Ensure prompt and accurate entry of inventory transactions
5. Take physical inventory count on a regular basis
6. Reconcile inventory discrepancies in a timely manner (use cycle counting)

## Slide 14: The MRP Matrix
Item
Gross Requirements
Scheduled Receipts
Projected On Hand
Net Requirements
Planned Order Receipts
Planned Order Releases
ITEM: LLC:
Lot Size: LT: PD 1 2 3 4 5 6 7 8 9

## Slide 15: Parts Of MRP Matrix
Item name or number identifying scheduled item
LLC low-level-code; lowest level at which item appears in a product structure
Lot size order multiples of this qty; can be min/max qty
LT (lead time)-time from order placement to receipt
PD (past-due)-orders behind schedule
Gross requirements-demand for item by time period

## Slide 16
Scheduled receipts
  quantity already on order & receipt date
  released orders become scheduled receipts
Projected on hand - expected on-hand inventory at end of period
Net requirements - net amount needed after on-hand adjustments
Planned order receipts - net requirements adjusted for lot-sizing
Planned order releases - planned order receipts offset by lead time
Parts Of MRP Matrix

## Slide 17: MRP Example
Item On Hand Scheduled Receipts Lot Size MPS
A 10 0 1 100, period 8
B 5 0 1 - - -
C 140 0 150 - - -
A
LT=3
B (3)
LT=4
C (2)
LT=2

## Slide 18: MRP Matrices For A & B

## Slide 19: MRP Matrices For C

## Slide 20: Manufacturing Resource Planning (MRP II)
Extension of MRP
Plans all resources needed for running a business
Variations include
  Service Requirements Planning (SRP)
  Business Requirements Planning (BRP)
  Distribution Requirements Planning (DRP)

## Slide 21: MRP II Modules
Forecasting
Customer order entry
Production planning / master production scheduling
Product structure / bill-of-material processor
Inventory control
Material requirements planning
Capacity planning
Shop floor control
Purchasing
Accounting
Financial analysis

## Slide 22: Capacity Requirements Planning (CRP)
Computerized system that projects loads from the planned order releases of MRP
Creates load profile
Identifies underloads and overloads

## Slide 23
Feasible?
Marketing
Plan
Financial
Plan
Business
Plan
Production
Plan
No
more
Yes
MRP II Diagram

## Slide 24
Master production
schedule
Material requirements
planning
Capacity requirements
planning
Manufacture
Inventory
Shop floor
control
Purchase
orders
Work
orders
Feasible?
No
Yes
Feedback

## Slide 25: Advanced Planning & Control Systems
Enterprise Resource Planning (ERP)
  updates MRP II with relational DBMS, GUI & client/server architecture; covers entire enterprise
Manufacturing Execution Systems (MES)
  links business planning & mgmt control systems
Customer-Oriented Manufacturing Management Systems (COMMS)
  unites departments & suppliers around customer
  multi-plant planning, multiple languages & currencies

## Slide 26: Problems with MRP
Material requirements plan is first; capacity is an afterthought
MRP assumes fixed lead times
Excessive reporting requirements

## Slide 27: Prospects for MRP/MRP II
Coordinates strategy among different functional areas
Responds quickly to what-if? questions at various levels
BOM processors, purchase modules, & customer order entry are standard requirements for Manufacturing Information Systems
Monitors design & vendor quality, & customer service
Builds trust, teamwork, & better decisions
Cash-flow planning & profit/cost projections

## Slide 28: Hierarchical Planning Process
Items
Product lines or families
Individual products
Components
Manufacturing operations
Resource level
Plants
Individual machines
Critical work centers
Production Planning
Capacity Planning
Resource
Requirements Plan
Rough-Cut
Capacity Plan
Capacity
Requirements Plan
Input/Output
Control
Aggregate
Production Plan
Master Production
Schedule
Material
Requirements Plan
Shop Floor
Schedule
All work centers

## Slide 29: Master Production Schedule
MPS
Period
Item
1
2
3
4
5
6
7
8
Clipboard
86
93
119
100
100
100
100
100
Lapboard
0
50
0
50
0
50
0
50
Lapdesk
75
120
47
20
17
10
0
0
Pencil Case
125
125
125
125
125
125
125
125
What different strategies for
planning production are shown here?

## Slide 30: Modular Bill Of Material
X10
Automobile
Engines Exterior Interior Interior Body
(1 of 3) Color (1 of 8) (1 of 3) Color (1 of 8) (1 of 4)
4-Cylinder (.40) Bright Red (.10) Leather (.20) Grey (.10) Sports Coupe (.20)
6-Cylinder (.50) White Linen (.10) Tweed (.40) Light Blue (.10) Two-Door (.20)
8-Cylinder (.10) Sulphur Yellow (.10) Plush (.40) Rose (.10) Four-Door (.30)
Neon Orange (.10) Off-white (.20) Station Wagon (.30)
Metallic Blue (.10) Cool Green (.10)
Emerald Green (.10) Black (.20)
Jet Black (.20) Brown (.10)
Champagne (.20) B/W Checked (.10)

## Slide 31: Initial Load Profile
1 2 3 4 5 6
Time (weeks)
Normal
capacity
Hours of
capacity

## Slide 32: Adjusted Load Profile
1 2 3 4 5 6
Time (weeks)
Work an
extra shift
Push back
Push back
Pull ahead
Overtime
Hours of
capacity

## Slide 33: Calculating Capacity
2 copiers, 2 operators
5 days/wk, 8 hr/day
1/2 hr meals, 1/2 hr maintenance per day
Efficiency = 100%
Utilization = 7/9 = 87.5%
Daily capacity = 2 machines x 2 shifts x 8 hours/shift x 100% efficiency x 87.5% utilization
= 28 hours or 1,680 minutes

## Slide 34: Determining Load & Load %
10 500 5.2 0.08 5.2 + (500 x 0.08) = 45.2
20 1,000 10.6 0.10 10.6 + (1,000 x 0.10) = 110.6
30 5,000 3.4 0.12 3.4 + (5,000 x 0.12) = 603.4
40 10,000 11.2 0.14 11.2 + (10,000 x 0.14) = 1,411.2
50 2,000 15.3 0.10 15.3 + (2,000 x 0.10) = 215.3
2385.7 min
Load percent = 2,385.7 / 1,680 = 1.42 x 100% = 142%
Add another shift:
Daily capacity = 2 machines x 3 shifts x 8 hours/shift x 100% efficiency x 87.5% utilization = 42 hours or 2,520 minutes
Revised load percent = 2,385.7 / 2,520 = 0.9467 x 100% = 94.67%
Job Setup Run time Total
# Copies time (min) (min/unit) Time Load

## Slide 35: Remedies for Underloads
1. Acquire more work
2. Pull work ahead that is scheduled for later time periods
3. Reduce normal capacity

## Slide 36: Remedies for Overloads
1. Eliminate unnecessary requirements
2. Reroute jobs to alternative machines or work centers
3. Split lots between two or more machines
4. Increase normal capacity
5. Subcontract
6. Increase the efficiency of the operation
7. Push work back to later time periods
8. Revise master schedule

## Slide 37: Splitting Orders
Lathes overloaded, shift work to milling
Machine Setup time Run time
Lathe 30 min 5 min
Mill 45 min 10 min
Three options for producing parts
1. Produce 100 units on lathe
2. Split 50:50 between lathe & mill
3. Optimal split between lathe & mill

## Slide 38: Options 1 And 2
1. Produce 100 units on lathe
  30 + 5(100) = 530 min
2. Split 50:50 between lathe & mill
  30 + 5(50) = 280 min on lathe
  45 + 10(50) = 545 min on mill
Job completion time = 545 minutes

## Slide 39: Option 3
3. Optimal split: x on lathe, 100-x on mill
  30 + 5x = 45 + 10(100-x)
  5x = 15 + 1000 - 10x
  15x = 1015
x = 67.66 or 68 units on lathe,(100-x) = 32 units on mill
  30 + 5(68) = 370 min on lathe
  45 + 10(32) = 365 min on mill
Job completion time = 370 minutes

## Slide 40: Capacity Requirements Planning
MRP planned
order releases
Routing
file
Capacity
requirements
planning
Open
orders
file
Load profile for
each machine center

## Slide 41: Capacity Terms
Load profile - compares released and planned orders with work center capacity
Capacity - productive capability; includes utilization and efficiency
Utilization - % of available working time spent working
Efficiency - performance compared to a standard
Load - the standard hours of work assigned to a facility
Load percent - the ratio of load to capacity

## Slide 42: The Alpha Beta Company
Item On Hand Scheduled Receipts Lot Size MPS
A 10 0 1 100, period 8
B 5 0 1 200, period 6
C 140 0 150 - - -
D 200 250, period 2 250 - - -
A
LT=3
C (3)
LT=4
D (2)
LT=2
D (3)
LT=2
B
LT=2

## Slide 43: MRP Matrices For A & B

## Slide 44: MRP Matrices For C & D

## Slide 45: Alpha Beta Planned Order Report
Period Item Quantity
1 C 150
2 D 250
3 D 250
4 B 195
5 A 90